| Obtain permission from instructor before operating this machine |  | Radial Arm Saw |
| --- | --- | --- |

Safety suggestions

- Eye protection must be worn at all times.

- Ensure that all machine guards are in place and that the saw travels freely on the arm                  before turning on the saw.

- Adjacent to the blade, the stock must be flat on the                                                       table and its back edge supported by the fence.

- Apply pressure on to the fence with your left hand                                                 while controlling the saw with your right.

- Return the saw to the rear of the table on                                                                 completion of the cut.

.

Radial Arm Saw

### Name    …………………..

### Class  …………………….

### Date ………………………

# Safety Quiz

| 1. | Stock must rest securely on the table and along the fence. | T | F |
| --- | --- | --- | --- |
| 2. | The saw tends to self-feed toward the operator. | T | F |
| 3. | Apply pressure toward the fence with your left hand when cross cutting. | T | F |
| 4. | Maintain a minimum distance of 4” (100 mm.) between your left hand and the blade path. | T | F |
| 5. | Return the saw to the rear of the table on completion of the cut | T | F |
| 6. | You may leave the machine as soon as the power is turned “Off”. | T | F |

# Text boxes

Cutting wood to length

Feed Direction

Fence

Fence

Blade guards

Kickback guard

2.

1.

3.

4.

5.

Handle

Arm