## Slide 1: Sheet Metal Box
CATA Skills Workshop – June 23, 2011
Dick Piersma
Mike Spiess

## Slide 3
Begin by establishing a “working edge” that you will make the majority of your measurements from. Here we chose the bottom edge.

## Slide 4
Here we added a “center line” that can be used to measure from if an edge is not square with your “working edge”. Make sure the “center line” is perpendicular to the “working edge”.

## Slide 5
This slide shows the cut-out of the project along with the tools needed to complete the task.

## Slide 6
Once the project is cutout, flatten the raised edges and then smooth with a file.

## Slide 7
Flattening usually is needed in the corners where your cuts meet from 2 directions.

## Slide 8
Make sure you smooth all edges, and from both sides. Carefully touch the edges to check for smoothness.

## Slide 9
Now the project is ready to bend. Mark each line as to the angle it will be bent (for reference).

## Slide 10
Typically you make your safety bends first. These bends will be 180° so the edge will be flat, but without a sharp edge.

## Slide 14
Next you will make the bends to begin shaping the box. In most cases, make the longest bends first.

## Slide 16
Side view showing approximate 90° bends.

## Slide 17
Top view showing how to set the “fingers” to make the box bends.

## Slide 18
Bends complete. Options here can be to have the tabs on the outside as shown here, or on the inside.

## Slide 19
After making the bends on the pan break, use a ball peen hammer to “gently” hammer the corners so that the tabs are tighter and that the box is square. You are now ready to fasten the corners.